## Slide 1
Christian Mandel
Bremen Ambient Assisted Living Lab Cyber Physical Systems
People Tracking in Ambient Assisted Living Environments Using low-cost Thermal Image Cameras
14th International Conference On Smart homes and health Telematics
Inclusive Smart Cities
And Digital health

## Slide 2
Overview
People Tracking Using low-cost Thermal Image Cameras
Problem Formulation
Problem-Solving Approach
System Overview
Sensorial Equipment
Raw Images
Image Preprocessing
Data Association
Particle Filter Steps
Experimental Evaluation

## Slide 3
People Tracking Using low-cost Thermal Image Cameras
Problem Formulation
Localize people in the Bremen Ambient Assisted Living Lab
Do not equip people with beacons such as RFID, BLE, ...
Make people´s localization pose accessible by infrastructure

## Slide 4
Problem-Solving Approach
Mount downward facing thermal camera at ceiling
Percepts given by segmented pixel-clusters
Pose estimation realized with M.-C. particle filter
People Tracking Using low-cost Thermal Image Cameras

## Slide 5
System Overview
Image Acquisition
Moving Average Subtraction
Segmentation
Data Association
PF Sensor Update
PF Motion Update
PF Resampling
Perception based on Thermal Images
Data Association handles
  Single Target – Multiple Measurements
  Multiple Targets – Single Measurement
Monte Carlo Tracking Filters
People Tracking Using low-cost Thermal Image Cameras

## Slide 6
FLiR Lepton camera module (900-14,000 nm)
Thermal sensitivity < 50 mK
51°horizontal FOV
80(h) × 60(v) pixels
Outputs 14 bit temperature relative to sensor`s temperature
Connects to Raspberry PI via Serial Peripheral Interface (SPI)
Sensorial Equipment
People Tracking Using low-cost Thermal Image Cameras

## Slide 7
Raw Images contain
High spatial frequency noise
Temperature gradient across whole image
Non person-related sources of heat
person
person
People Tracking Using low-cost Thermal Image Cameras

## Slide 8
Moving Average Subtraction
Removes static sources of heat and temperature gradient
person
person
People Tracking Using low-cost Thermal Image Cameras

## Slide 9
Segmentation
Percept given by pixel blob showing thermal contrast against background
Percept contains
  Pixel elements
  Center coordinates
  Radius
person
person
People Tracking Using low-cost Thermal Image Cameras

## Slide 10
Data Association
two persons obstructed by ceiling beam
two persons obstructed by ceiling beam
person 1 described by two percepts
person 2 described by one percept
Single Target – Multiple Measurements
People Tracking Using low-cost Thermal Image Cameras

## Slide 11
Data Association
Single Target – Multiple Measurements
Multiple Targets – Single Measurement
two persons close to each other
two persons close to each other –
described by one percept
People Tracking Using low-cost Thermal Image Cameras

## Slide 12
Data Association
Single Target – Multiple Measurements
Multiple Targets – Single Measurement
Use Circle-Circle intersection criterion to associate percept to sample
Instantiate new filter for unassociated percepts
percept 1
percept 2
sample 1
percept 3
sample 2
sample 3
People Tracking Using low-cost Thermal Image Cameras

## Slide 13
Particle Filter Steps
Sensor Update
Motion Update
ω-based Resampling
People Tracking Using low-cost Thermal Image Cameras

## Slide 14
Experimental Evaluation
People Tracking Using low-cost Thermal Image Cameras
Compare paths tracked by A.R.T. DTrack2 and TIMHT
DTrack2 tracks spherical markers (Ø 30mm ) attached to target
Small tracking workspace due to thermal camera´s low FOV

## Slide 15
Experimental Evaluation
People Tracking Using low-cost Thermal Image Cameras
Tracked path of approx. 23m length

## Slide 16
People Tracking Using low-cost Thermal Image Cameras
Experimental Evaluation
min/max/mean error:

## Slide 17
Experimental Evaluation
Screencast of logfile replay
Two people walking around in the BAALL
People Tracking Using low-cost Thermal Image Cameras

## Slide 18
Thank You
People Tracking Using low-cost Thermal Image Cameras
Future Work
Combination of multiple thermal image cameras, and/or application of wide FOV lenses
Dynamic segmentation threshold adjustment
Shape-based pixel-blob classification
Deeper integration into BAALL and system tests